## Slide 1
K-Nearest Neighbor Digit Recognition
Application | Domain | Constraints | Kernels/Algorithms
Voice Removal and Pitch Shifting | Audio Processing | Latency (Real-Time) | FFT, Inverse FFT, DSP Filters
DNA and Protein Sequencing | Bioinformatics | Throughput | Smith Waterman
Advanced Encryption Standard | Cryptography | Throughput | Matrix Substitutions and Permutations
Monte Carlo Option-Pricing | Financial Analysis | Throughput / Latency | Black Scholes, Mersenne Twister, Box Muller
Digit Recognition | Machine Learning | Throughput | Population-Count, K-NN, K-Means
Convolutional Neural Networks | Machine Learning | Throughput | Convolution, Soft Max and Max Pool Layers
Face Detection | Video Processing | Throughput | Viola Jones Algorithm
Lane Detection | Video Processing | Latency (Real-Time) | Edge Detection
Rosetta: A Realistic Benchmark Suite for Software Programmable FPGAs
Udit Gupta, Steve Dai, Zhiru Zhang
Computer Systems Laboratory, Electrical and Computer Engineering, Cornell University, Ithaca, NY
Proposed Initial Benchmarks for Rosetta
Realistic benchmarks are important for the development of sophisticated yet scalable high-level synthesis (HLS) tools that allow FPGAs to be programmed in software while achieving high-performance designs.
We propose a suite of realistic software applications with enforceable system-level hardware constraints to model hardware accelerators targeting heterogeneous FPGAs.
We present a C and OpenCL based design and verification flow that accommodates both the sequential and parallel programming models commonly supported by HLS.
Overview
Our Research
Productivity
Performance
C-to-gates
Manual
RTL
CPU/GPU
Programming
~2-3X
Efficiency
gap
~5-10X
Productivity gap
Programming
FPGAs?
Software
Programming
Hardware
Design
Image courtesy of Xilinx, 2015
Modern FPGAs are heterogeneous SoCs composed of multi-core processors, hardened IPs, and reconfigurable fabric.
Calls for an unprecedented amount of software programmability as FPGA emerges from a logic to computing device.
Modern FPGAs and HLS Tools
Insufficient QoR compared to hand-written RTL and significant productivity gap from pure software programming.
Needs significant amount of manual code transformations and lacks automatic compiler and synthesis optimizations for performance.
Realistic: Representative application domains with large applications and user enforceable design constraints.
Reducible: Users can profile applications and sub-kernels for effectively benchmarking QoR.
Retargetable: Supports various HLS tools which target multiple substrates and FPGA devices.
The Three R’s of Rosetta
Span a limit ed subset of computing domains that FPGAs target and consist of small kernels (less than 1000 lines) which lack the complexity representative of common HLS designs.
Provide no support for multiple programming models and require significant user overhead in adding HLS-specific optimization directives.
Do not allow convenient parameterization of designs by user.
Existing HLS Benchmark Suites
for digit in range (0, 10):
for training_inst in training_data[digit]:
diff = training_inst xor test_inst
distance = population_count(diff)
if (distance < min):
nearest_neighbor = training_inst
min = distance
return nearest_neighbor
Efficient hardware for population count kernel.
Parallel execution (by loop unrolling) across digits 0-9.
Pipelined execution over training instances.
Partitioned training data increases memory bandwidth.
Synthesized System Architecture
Source Data
Source Code
Baseline Software Design
OpenCL Harness
OpenCL Kernels
C/C++ Harness
C/C++ Kernels
Rosetta Harness
HLS
Software Simulation
HLS Optimizations
Realistic Design Constraints
Hardware/Software Co-Simulation
Retargetable FPGA Implementation
Reconfigurable Fabric
Host Processing System
Synthesized Hardware Accelerator
Host Application
Rosetta Development Flow and Application Architecture
Development Flow
C-based application-specific kernels can easily be added to the generic harnesses.
Synthesis results are used to optimize designs given design constraints.
FPGA Implementation
Host Application - Responsible for controlling the system and accelerator
Kernels - Consist of the compute intensive portions of the applications to be accelerated.